## Slide 1: Cubit for Accelerator Modeling
Stanford, March 27-31, 2023
Computational Electrodynamics Department
SLAC National Accelerator Laboratory
More information at
https://cubit.sandia.gov/tutorials
Or
https://coreform.com/products/coreform-cubit/tutorials/

## Slide 2: Outlook
CUBIT Basics
Modeling – A Pillbox Cavity
  Model generation with GUI
  Model generation with command syntax in journal file
Meshing – A Quarter of Pillbox Cavity
  Create mesh journal file
  Edit mesh journal file with GUI
  Tips for meshing
Acdtool – Converting Mesh Format (*.gen -> *.ncdf)
Paraview – Visualize meshes (Option)

## Slide 3: Cubit Basics
CUBIT is a geometry and mesh generation toolkit developed by Sandia National Laboratories
CUBIT can import and create geometries in many formats such as ACIS, IGES, and STEP
CUBIT can generate meshes for finite element codes such as ACE3P

## Slide 4: Cubic - Model Generation
Seven primitive types are available and accessed with the Create button in GUI or command syntax.
CUBIT can create many analytic geometry types
from scratch and in decomposition.
CUBIT can create Bottom-Up geometries from a collection of lower order entities, such as creating vertices, then curves, then surfaces. Volumes can be created by sweeping or bonding surfaces .

## Slide 5: Cubit - User Interfaces (GUI)
Command Panels
Toolbars
Graphics Window
Command Line
Launch cubit (double click Cubit icon)
Entity Tree
Properties Page
Read “Tip Of The Day” and Close it

## Slide 6: Selecting Your Working Directory
Click File -> Set Directory,
select working directory (/pillbox)
Click “Select Folder”
Or type the directory in command line

## Slide 7: Drop Down Menus
Drop Down Menus provide functions such as file management, edit controls, user preferences, display options, journal file management, and help.

## Slide 8: Toolbars
Zoom in, out, and fit
Geometry entity Selection Filter
Mesh entity selection
undo
Display modes
Toolbars provide the most commonly used features by clicking toolbar icons.
When an entity is selected, that entity will become highlighted.
Boundary condition selection

## Slide 9: Command Panels
Every command entered with buttons in the GUI version is available in CUBIT’s command language in the command line workspace.
Press an Icon to enter a new mode, each button press takes you to a lower level
- Geometry: Create, modify, cleanup…
- Meshing: Intervals, schemes, smoothing…
- Materials and BCs: sidesets, blocks …
- Analysis Setup: Export mesh
- Post Processing: Customizable shortcut

## Slide 10: Command Line Workspace
All commands can be entered in the command window at the CUBIT>prompt. Partly words OK. Need help? CUBIT> Help XXX
Error window: lists error information.
History window: lists the last 100 command lines.

## Slide 11: Pillbox Cavity
L-Band Pillbox:
Height = 90 mm
Radius = 100 mm
Beam pipe:
Radius = 35 mm
Disk:
Radius=12mm
TM010: f ~ 1.2GHz,
λ~ 250mm

## Slide 12: Modeling a Pillbox Cavity with GUI
Step 1
Step 2
Step 3
Step 4
Step 5

## Slide 13: Step 1: Create a Pillbox Cell
click Mode-Geometry
click Entity-Volume
click Action-Create
select Cylinder
enter Values for Circular
hit Apply
Use smaller units when creating and meshing the model to avoid tolerance problems, and scale to meters later for ACE3P calculation.
1
2
3
4
5
6

## Slide 14: Display the Pillbox Cell
Or type “create cylinder height 90 radius 100” in the command line window.

## Slide 15: Adjust the Graphics Display
right-button to Pan
left-button to Rotate
middle-button to Zoom
Using 3 button mouse

## Slide 16: Step 2: Add Beampipe to the Pillbox Cell
Transparency view
Or type “create cylinder height 300 radius 35” in the command line window.

## Slide 17: Geometry Booleans
Geometry Booleans define the shape of a body based on overlapping regions :
  Subtract
    Remove regions of overlap
  Intersect
    Remove regions that don’t overlap
  Unite
    Combine all regions into one body

## Slide 18: Step 3: Unite Beampipe and Pillbox Cell
Good to “compress ids” after “unite” or “delete” entries
5
Or type “unite vol 1 2”, and then “compress ids” in the command line window.
2
3
4
Under Geometry Mode-Volume Entity,
click Action-Boolean
select Unite
enter Volume IDs {1 2}
hit Apply

## Slide 19: Select One or a Group of Curves
Selecting Curve
Put curser on curve, click Left button to pick, the curve ID will be shown in Command Line window.
Similarly for selecting a surface or volume

## Slide 20: Rounding the Iris of the Pillbox Cavity
6
2
3
4
5
7
1
Or type “modify curve 5 6 blend radius 12” in the command window.
Under Geometry Mode,
click Entity-Curve
click Action-Modify
select Blend/Chamfer
enter Curve IDs {5 6}
Select Blend
Enter value {12} for Blend radius
hit Apply

## Slide 21: Display the Pillbox Cavity

## Slide 22: Geometry Webcutting
Geometry Webcutting slices 1 Body into 2 Bodies
  - Plane
  - Cylindrical surface
  - Extended surface
  - Intersection with “Tool” body
Webcut with yzplane, delete unneeded body
Webcut with xzplane, delete unneeded body

## Slide 23: Step 4: Reduce ½ of the Pillbox Cavity
Under Geometry Mode
Click Entity-Volume
Click Action-Webcut;
Select Coordinate Plane;
Enter Volume ID {1};
Choose YZ Plane;
Offset value 0 (default)
Apply
2
3
4
6
Or type “webcut vol 1 with xplane ” in the command window.
1
5
7

## Slide 24: Delete Unneeded Volume
1
2
3
del vol 2
compress ids
4
Good to “compress ids” after “unite” or “delete” entries
Under Mode-Geometry, Volume-Entity
Click Action-Delete;
Enter Volume ID {2};
Apply

## Slide 25: Step 5: Reduce 1/4 of the Pillbox Cavity
1
2
3
Del volume 1
Compress ids
webcut vol 1 with yplane
Good to “compress ids” after “unite” or “delete” entries

## Slide 26: Save the Model in ACIS (.sat) Format
Click File option from Drop Down Menu
Choose Export…
Choose *.sat format
Enter file name: pillbox
Hit “Save”
Choose Export all
Hit Finish

## Slide 27
Modeling a Pillbox Cavity with Journal Files
Every command entered with buttons in the GUI version or typed in command window has been recorded in CUBIT’s command language in command tab as well as listed in history tab
Collect and edit these commands in a journal file, and run through the commands in the journal file by “play” it

## Slide 28
Tools
Tools -> Journal Editor
In Journal Editor window: File -> Import -> Command Tab
save to a file as *.jou format (eg. step1-Make-pillbox.jou)
Create Pillbox Cavity Journal File

## Slide 29: Edit Journal File: step1-Make-pillbox.jou
reset
#cavity dimensions
#{cav_length = 90}
#{cav_radius = 100}
#{bp_length = 300}
#{bp_radius = 35 }
#{iris_rounding = 12}
create Cylinder height {cav_length} radius {cav_radius}
create Cylinder height {bp_length} radius {bp_radius}
unite volume 1 2
compress ids
modify curve 6 5 blend radius {iris_rounding}
webcut volume 1 with plane xplane offset 0 noimprint nomerge
delete volume 2
compress ids
webcut volume 1 with plane yplane offset 0 noimprint nomerge
delete volume 1
compress ids
export acis "pillbox.sat" overwrite
Define variables
Replace numbers with variables in {}
Add “reset” at top to clean up the workspace when “play” the step1-Make-pillbox.jou
step1-Make-pillbox.jou
Add “overwrite” to replace previous one

## Slide 30: Play the Journal file to Create a Pillbox Cavity
play
Tools->play journal files: select “step1-Make-pillbox.jou”

## Slide 31
Cubic - Mesh Generation
Solid model: pillbox.sat
vol all scheme tetmesh
block all element type tetra10
tetrahedral mesh with quadratic surface for complicated structure modeling

## Slide 32: Import the Solid Model (*.sat) - check and fix bad geometries using power tools (see tips for meshing) - imprint and merge body all if there are multi volumes Choose Tet mesh scheme Set the mesh interval (~wavelength/10, ~bunch length/3) and generate tetrahedral mesh - check mesh quality Apply BCs at interior & exterior surfaces - check sidesets Set block IDs for volume material attributes - check blocks Set element type tetra10 Scale units if needed export the mesh (*.gen)
Orders can be exchanged
Meshing Process

## Slide 33: Create Mesh Journal File
Reset
Cd: “your working directory”// pillbox in this directory
##import model
import acis "pillbox.sat"
##choose Tet mesh
vol all scheme tetmesh
##uniform or adaptive meshes
##Volume 1 size 10
volume 1 sizing function type skeleton
mesh volume 1
##apply BC (1 & 2: ends of beampipe, 3& 4: sym. Planes)
sideset 1 surface X
sideset 2 surface X
sideset 3 surface X
sideset 4 surface X
#exterior surfaces
sideset 6 surface all except XXXX
##set block ID
block 1 volume all
##set block element type
block 1 element type tetra10
##scale units and export mesh
volume 1 scale 0.001
export genesis "pillbox.gen" overwrite
step2-Mesh-pillbox.jou

## Slide 34: Open the Mesh Journal File
1. Click File -> Set Directory,
select working directory
2. Click Tools -> Journal Edit
3. Click Open- >
open step2-Mesh-pillbox.jou

## Slide 35: Play and Edit the Mesh Journal File
Play the commands in step2-Mesh-pillbox.jou and edit as needed.
Highlight through each command, right click, select “Play Selected”

## Slide 36
Uniform Meshes
Generate a few meshes with different mesh qualities and do mesh convergence study
vol 1 size 10
Mesh vol 1

## Slide 37
Delete Unsatisfied Mesh
1
2
3
Mode-Mesh
Entity-Volume
Action-Delete
Volume ID(s) {1}
Apply
4
5
Or type “del mesh vol 1” in the command window.

## Slide 38
Adaptive Meshes
Basic Arguments
max_size (default=auto): The value for max_size is calculated automatically by default.
min_size(default=auto): The value for min_size is calculated automatically by default.
max_gradient (1.0 to 3.0, default 1.5): The transition in element size is controlled using this parameter. Larger values of max_gradient result in fewer elements, but also lead to more abrupt transitions in size and possibly poorer quality elements.
Scaling and Accuracy Arguments:
scale (1 to 10, default 7): The overall size of the elements is controlled by this argument. A coarser mesh can be generated by increasing the value of scale up to 10.0. To get a finer mesh, decrease the value of the scale (minimum value = 1).
time_accuracy_level (1 to 3, default 2): This controls the computational time and accuracy level by adjusting various internal parameters of the skeleton sizing function. Users should try levels in increasing order. Level 1 takes the shortest time to compute the skeleton sizing function and Level 3 takes the longest time to compute the skeleton sizing function.
file:///Applications/Cubit-16.04/Cubit.app/Contents/MacOS/help/cubithelp.htm
volume 1 sizing function type skeleton min_size 6 max_size 10 max_gradient 1 scale 5

## Slide 39
Select One or a Group of Surfaces

## Slide 40: Apply BCs at Interior & Exterior Surfaces
Define the end of the right beampipe
Sideset 1 surface 2
Define symmetry plane 1
Sideset 3 surface 3
Define symmetry plane 2
Sideset 4 surface 1
Define exterior surfaces
Sideset 6 surface all except 2 4 3 1
Define the end of the left beampipe
Sideset 2 surface 4

## Slide 41: Set Block ID for Volume Material Attributes
Mode-Exodus ->Manage Material and Exodus Entity ;
Entity-Block -> Manage Exodus Block;
Action-Manage -> Action Block;
Add;
Block ID {1};
Volume;
IDs {all}; or {1}
Apply
1
2
3
4
5
6
7
8
Or type “block 1 vol 1” in the command window.

## Slide 42: Check BCs and Mesh Quality

## Slide 43: Tips for Meshing
Check and clean models first using power tools
Imprint and merge body all before meshing for a multivolume model
Group merged surfaces using command group “name” add surface with is_merged
Mesh smaller surfaces first, which have good mesh representation
Sometimes it is good to separate one volume into multi-volumes and mesh them with different mesh element sizes and sizing functions
Smooth transition from coarse to dense regions
Start with a coarse mesh and refine the mesh to check accuracy
  Check mesh quality using “quality vol all distortion”

## Slide 44
Working Flow Before Running ACE3P
Step1-Model-pillbox.jou -> pillbox.sat  step2-Mesh-pillbox.jou -> pillbox.gen
pillbox.ncdf
ACE3P
acdtool
Paraview on local machine
Acdtool and ACE3P on NERSC
Cubit on local machine

## Slide 45: acdtool is a collection of tools to do prep/post processing. Acdtool for prep-processing: acdtool meshconvert *.gen
Acdtool - Converting Mesh Format
convert cubit mesh in GENESIS format to SLAC ncdf format mesh
exam mesh statistics, quality, and correctness
check and remove invalid second order tetrahedral elements
Invalid element

## Slide 46
Your Working Directory on NERSC-Perlmutter
Logging to Perlmutter
  from the terminal run the command
      Local $ ssh <username>@perlmutter-p1.nersc.gov
      <username> is you NERSC user ID
Go to your cw23/example/cubit/pillbox cubit directory
  cd cw23/exercise/cubit/pillbox
Transfer files to NERSC Computer
  scp <srcfile> <username>@Perlmutter-p1.nersc.gov:<dstpath>
  scp pillbox.gen <username>@ Perlmutter-p1.nersc.gov: /pscratch/sd/l/lge/cw23/exercise/cubit/pillbox
  scp run-meshconvert.batch <username>@ Perlmutter-p1.nersc.gov: /pscratch/sd/l /lge/cw23/exercise/cubit/pillbox

## Slide 47
Run acdtool on NERSC-Edison
Submit job: sbatch run-meshconvert.batch
Once your job done, pillbox.ncdf will be generated.
Check acdtool.log for mesh quality
#!/bin/bash -l
#SBATCH -C cpu
#SBATCH -q shared
#SBATCH -A m349
#SBATCH -t 00:10:00
#SBATCH -J myjob
#SBATCH -e ace3p.e%j
#SBATCH -o ace3p.o%j
export DIR=$PWD
cd $DIR
srun -n 1 --cpu-bind=cores /global/cfs/cdirs/ace3p/perlmutter/CPU/acdtool meshconvert pillbox.gen

## Slide 48
Acdtool.log
If Euler Char is not OK, do not use it for ACE3P simulation. The mesh has some problems. For example, sidesets are incomplete or overlap each other.
If aspect ratio > 20, shape measure <0.01, it might take longer time to get the results from ACE3P.

## Slide 49
Visualize Meshes in Paraview
Transfer back your mesh file (pillbox.ncdf) to your local machine
Launch paraview
Load SLAC tool box from tool menu -> manage plugin -> SLACTools

## Slide 50
Visualize Imperfect Meshes in Paraview
If there are some bad elements in mesh, there will be a warning in acdtool.log, such as larger aspect ratio, small shape measure, and *.vtu files will be generated.
Load these files in Paraview to see where they are, and where you should refine the mesh.
Load *.ncdf file;
File -> open, select one *.vtu file to open;
Edit *.vtu mesh color
Make *.ncdf mesh in transparent