## Slide 1: S3P Tutorials
CW23 - Stanford, March 27-31, 2023
Computational Electrodynamics Department
SLAC National Accelerator Laboratory

## Slide 2: S3P Capability
Calculates scattering parameters of RF components
Typical applications
  Waveguide component matching
  RF load
  Traveling wave accelerator structure coupler design

## Slide 3: S Parameter Solver
a1,a2…
b1,b2…
bn,bn+1…
an,an+1…
bm,bm+1…
am,am+1…
a: input wave
b: reflected wave
[b]=[S][a]
S: scattering matrix
Port: a reference point on a waveguide. Properties set to simulate infinite long waveguide
S-Parameter Equation

## Slide 4: S3P Examples
90 degree bend
Waveguide load
Window

## Slide 5: S3P Practice 1: XBand Mitered Bend
1) model 2) mesh
3) Solver 4) postprocess
Run S3P
Dimensions
(WR90): 22.86X10.16
22.86
60
16
R1
R5
10.16

## Slide 6: Steps to Create the Model
Create “brick”: 10.16 X 22.86 X 60
Move (dx,dy,dz): 0, 0, {0.5*60-0.5*22.86}
Create “brick”: 10.16 X 60 X 22.86
Move (dx,dy,dz): 0, {0.5*60-0.5*22.86},0

## Slide 7: Now Add Chamfer and Rounding
Unite all (remember to “compress ids”
Cut corner (chamfer) with “radius” 16

## Slide 8: Add “Tool” Roundings
Blend “sharp corner” with radius 1
Blend “chamfered corners” with radius 5
Then “export” the model

## Slide 9: JOU File to Create 90 Degree Bend
reset
brick x 10.16 y 22.86 z 60
move volume 1 location x 0 y 0 z {0.5*60-0.5*22.86}
brick x 10.16 y 60 z 22.86
move volume 2 location x 0 y {0.5*60-0.5*22.86} z 0
unite all
compress ids
modify curve 6 chamfer radius 16
modify curve 11 blend radius 1
modify curve 20 22 blend radius 5
export acis “90DegreeBend.sat" overwrite

## Slide 10: Parameterized JOU File
reset
#{wgwidth = 22.86}
#{wghight = 10.16}
#{wglength = 60.0}
#{cornercut = 16}
#{rcorner1 = 1}
#{rcorner2 = 5}
brick x {wghight} y {wgwidth} z {wglength}
move volume 1 location 0 0 {0.5*wglength-0.5*wgwidth}
brick x {wghight} y {wglength} z {wgwidth}
move volume 2 location 0 {0.5*wglength-0.5*wgwidth} 0
unite all
compress ids
modify curve 6 chamfer radius {cornercut}
modify curve 11 blend radius {rcorner1}
modify curve 20 22 blend radius {rcorner2}
export acis “90DegreeBend.sat" overwrite

## Slide 11: Modify “Mesh-pillbox.jou” to Mesh the Bend
reset
import acis "90DegreeBend.sat"
volume all scheme Tetmesh
volume all sizing function type skeleton scale 5 time_accuracy_level 2 min_size auto max_size 3 max_gradient 1.2
mesh volume all
Sideset 7 surface 10
Sideset 8 surface 12
Sideset 6 surface all except 10 12
block 1 volume all
block 1 element type tetra10
volume all scale 0.001
export Genesis "90DegreeBend.gen" block all overwrite
TIP: copy and modify an existing meshing journal file

## Slide 12: The Mesh
Front surface visibility off
(in CUBIT)
mesh adapted to curvature of surface

## Slide 13: S3p input – 90DegreeBend.s3p
ModelInfo: {
File: ./90DegreeBend.ncdf
BoundaryCondition: {
Exterior: 6
Waveguide: 7, 8
}
}
FiniteElement: {
Order: 1
CurvedSurfaces: on
}
FrequencyScan: {
Start: 9.424e+9
End: 14.424e+9
Interval: 0.2e+9
}
PostProcess: {
Toggle: on
PortNumber: 7
//only save mode file for port with
//this reference number;
}
Port: {
ReferenceNumber: 7
NumberOfModes: 1
}
Port: {
ReferenceNumber: 8
NumberOfModes: 1
}

## Slide 14: Input: ModelInfo
ModelInfo: {
File: ./bend.ncdf
BoundaryCondition: {
Exterior: 6
Waveguide: 7, 8
}
}
Two ports: reference 7 and 8

## Slide 15: Input: FrequencyScan
FrequencyScan: { //enable frequency scan of S parameter
Start: 9.424e+9
End: 14.424e+9
Interval: 0.2e+9
}
// if “Start” = “End”: perform single frequency S parameter computation

## Slide 16: Input: Port Information
Port: {
ReferenceNumber: 7
NumberOfModes: 1
}
// NumberOfModes : number of modes to load for this port
// Use the cutoff frequencies to estimate how many modes need to be loaded

## Slide 17: Input: PostProcess
PostProcess: {
Toggle: on // on or off
PortNumber: 7 // save mode files for this port excitation
// ModeFile: rec // mode file name: rec.port#.modeN,
// modeN indicates Nth port mode;
// default mode file name: s3p.port#.modeN,
}
Specify the input port and compute the field distributions.
If specified: only save mode files for port excitation with the specified reference number
If not specified, save mode files for all the ports

## Slide 18: Run s3p
Copy 90DegreeBend.ncdf to NERSC
Copy run-s3p.batch to NERSC
$ sbatch run-s3p.batch
s3p result is written into subdirectory: s3p_results
#!/bin/bash -l
#SBATCH -C cpu
#SBATCH -q debug
#SBATCH -A m349
#SBATCH -N 1
#SBATCH -t 00:10:00
#SBATCH -J s3p_run
#SBATCH -e myjob.%j.err
#SBATCH -o myjob.%j.out
#SBATCH --ntasks-per-node=4
export DIR=$PWD
cd $DIR
srun -n 4 -c 4 --cpu-bind=cores /global/cfs/cdirs/ace3p/perlmutter/CPU/s3p 90DegreeBend.s3p
run-s3p.batch

## Slide 19: Files in s3p_results Directory
Filenames | Description
PortRef7.out PortRef8.out | Port mode, can be used to examine the waveguide modes
Reflection.out | S-parameter - amplitude
Sparameter.out | S-parameter - complex
port_7 port_8 | 2d port files
s3p.port7.mode0.f1.042400E+10.mod s3p.port7.mode0.f1.062400E+10.mod s3p.port7.mode0.f1.082400E+10.mod …. s3p.port7.mode1.f1.122400E+10.mod s3p.port7.mode1.f1.142400E+10.mod s3p.port7.mode1.f1.162400E+10.mod s3p.port7.mode1.f1.182400E+10.mod | Field files. “s3p” is the default prefix for the mod file, it will take the “ModeFile” as the prefix if specified in the input. “port7.mode#” is the port mode ID
s3p.output | Log file
VECTOR | Directory – DOF coefficient

## Slide 20: Mitered Bend Paraview Visualization
Port mode E field (11.3424GHz)
Copy whole directory back to laptop (Warning: Many (larger) files)
$scp –r <username>@perlmutter-p1.nersc.gov:tmp/s3p/90DegreeBend/s3p_results ./.

## Slide 21: Mitered Bend TE10 S11
TE10 reflection

## Slide 22: S3P Practice 2 – recWG-load1
Model and mesh multi-volume geometry
Lossy material specification

## Slide 23: S3P Practice 2 – recWG-load1
Model only half the geometry
Magnetic Symmetry plane
Model a waveguide load with the following geometry
Calculate S11 from 2.456GHz to 3.056GHz
200 mm
WR284
72.136X34.036

## Slide 24: Model: step1-Make-recWG-load1.jou
reset
##wr284
##wguide: 2.84*fsc0=72.136
##hguide: 1.34*fsc0=34.036
#{wwidth = 72.136}
#{wheight = 34.036}
#{loadl = 200.0 }
#{wlength = 150 }
##the port location is at 150
brick x {0.5*wwidth} y {wheight} z {loadl}
body 1 move {0.25*wwidth} 0 {-0.5*loadl}
webcut volume 1 with plane vertex 5 vertex 6 vertex 3
brick x {0.5*wwidth} y {wheight} z {wlength}
body 3 move {0.25*wwidth} 0 {0.5*wlength}
unite 2 3
compress ids
export acis "recWG-load1.sat" overwrite

## Slide 25: Mesh: step2-Mesh-recWG-load1.jou
reset
import acis "recWG-load1.sat"
imprint body 1 2
merge body 1 2
volume all scheme tetmesh
surface all scheme triadvance
volume 1 size 8.0
volume 2 size 8.0
## interface surfaces
surface 1 size 8.0
surface 1 interval hard
mesh volume 1
mesh volume 2
smooth vol all
smooth surface all
sideset 1 surface 5 7
sideset 7 surface 6
sideset 6 surface all except 5 7 6 1
block 1 vol 2
block 2 vol 1
block all element type tetra10
transform mesh output scale 0.001
export genesis "recWG-load1.gen" overwrite

## Slide 26: s3p input: recWG-load1.s3p
ModelInfo: {
File: ./recWG-load1.ncdf
BoundaryCondition: {
Magnetic: 1
Exterior: 6
Waveguide: 7
}
Material : {
Attribute: 1
Epsilon: 1.0
Mu: 1.0
}
Material : {
Attribute: 2
Epsilon: 10.0
Mu: 1.0
EpsilonImag: -1.52
}
SurfaceMaterial: {
ReferenceNumber: 6
Sigma: 5.8e7
}
}
FiniteElement: {
Order: 1
CurvedSurfaces: on
}
FrequencyScan: {
Start: 2.456e+9
End: 3.056e+9
Interval: 0.05e+9
}
PostProcess: {
Toggle: on
PortNumber: 7 // save mode files for this port
}
Port: {
ReferenceNumber: 7
NumberOfModes: 2
}

## Slide 27: s3p result: Reflection.out

## Slide 28: S3P Practice 5 - Window
Model ¼ geometry
3
33
120
r=9.37
Material : {
Attribute: 1
Epsilon: 1.0
Mu: 1.0
}
Material : {
Attribute: 2
Epsilon: 9.37
Mu: 1.0
}
vacuum
block
window
block
72.136X34.163
45

## Slide 29: S3P – Window: step1-Make-window.jou
reset
#{w284=72.136 }
#{h284=34.163 }
#{cradius = 45 }
#{wdwt = 3 }
#{cavl = 15 }
#{wlengthz = 60}
## ceramic window
brick x {w284} y {h284} z {2*wlengthz}
create cylinder height {2*cavl+wdwt} radius {cradius}
unite all
compress ids
webcut volume 1 with plane zplane offset {0.5*wdwt}
webcut volume 2 with plane zplane offset {-0.5*wdwt}
webcut volume all with plane xplane offset 0
delete volume 6 4 5
webcut volume all with plane yplane offset 0
delete volume 1 2 3
compress ids
export acis "window.sat" overwrite

## Slide 30: S3P – Window: step2-Mesh-window.jou (1)
reset
import acis "window.sat”
volume all scheme tetmesh
merge tolerance 0.0001
imprint body all
merge body all
volume 1 3 sizing function type skeleton scale 5 time_accuracy_level 2 min_size auto max_size 6 max_gradient 1.2
volume 2 sizing function type skeleton scale 3 time_accuracy_level 2 min_size 1.5 max_size 3 max_gradient 1.2
group 'ms’ add surface Is_merged
ms expand size 2
ms expand interval hard

## Slide 31: S3P – Window: step2-Mesh-window.jou (2)
mesh volume all
smooth vol all
smooth surface all
group "port7" add surface 16
group "port8" add surface 2
group "sym1" add surface 5 11 17
group "sym2" add surface 1 9 14
group "ss6" add surface all
ss6 subtract ms from ss6
ss6 subtract sym1 from ss6
ss6 subtract sym2 from ss6
ss6 subtract port7 from ss6
ss6 subtract port8 from ss6
sideset 1 surface in sym1
sideset 2 surface in sym2
sideset 7 surface in port7
sideset 8 surface in port8
sideset 6 surface in ss6
block 1 vol 1 3
block 2 vol 2
block all element type tetra10
transform mesh output scale 0.001
export genesis "window.gen" overwrite

## Slide 32: S3P – Window: window.s3p
ModelInfo: {
File: ./window.ncdf
BoundaryCondition: {
Magnetic: 1
Electric: 2
Exterior: 6
Waveguide: 7, 8
}
Material : {
Attribute: 1
Epsilon: 1.0
Mu: 1.0
}
Material : {
Attribute: 2
Epsilon: 9.37
Mu: 1.0
}
SurfaceMaterial: {
ReferenceNumber: 6
Sigma: 5.8e7
}
}
FiniteElement: {
Order: 2
CurvedSurfaces: on
}
FrequencyScan: {
Start: 2.356e9
End: 3.856e9
Interval: 0.1e+9
}

## Slide 33: S3P – Window: run & postprocess
Run s3p: input file “window.s3p”
Plot S11
Use “acdtool postprocess rf” to print out field along (x=0, y=0) and plot using other software, e.g. exel or gnuplot.
Visualize using Paraview
  Field contour plot
  Arrow plot
  Electric field along (x=0, y=0)

## Slide 34: S3P – Window: result – S11
S11 plot

## Slide 35: S3P – Window: window.rfpost
RFField
{
ResultDir = jobdir // Jobname
FreqScanID = 2 // For S3P only: frequency scan index
ModeID = 0
xsymmetry = magnetic // [none, electric, magnetic]
ysymmetry = magnetic // [none, electric, magnetic]
gradient = -1
cavityBeta = 1.00000 //for R/Q, V integral
reversePowerFlow= 0 // [1=charging 0=decaying]
x0 = 0.00000
y0 = 0.00000
gz1 = -0.03500
gz2 = 0.03500
npoint = 300
fmnx = 10
fmny = 10
fmnz = 50
}
ALLFieldOnLine
{
ionoff = 1
modeID1 = -1
modeID2 = -1
npoint = 300
filename = field1
rfphase = 0.00000
x1 = 0.00000
x2 = 0.00000
y1 = 0.00000
y2 = 0.00000
z1 = 100000000.00000
z2 = 100000000.00000
}

## Slide 36: S3P – Window: rfpost field
FreqScanID = 2 (F=2.556GHz)
Field file: field1_0.ec //”0” first port mode
The following figure is Ey along (0,0), window is at z=0

## Slide 37: S3P – Window: Paraview Visualization
Field amplitude contour
Ey plot along (0,0), window is at z=0